## Slide 1
  C115 L3 Training Slides
C115 L3 training slides

## Slide 2: Product Overview
        Technical Specification
        . GSM 900/1800 or 850/1900
        . Size = 72 cc
        . Weight < 80g
        . Display Pixel area 96x64
        . Battery 860mAH Li-ion removable
        . Antenna : Internal
Product Overview

## Slide 3
Chipset
U15 “RITA”
(Transceiver IC, TX/RX VCO)
U13 “SKY77324”
(PA + Matching)
U1 “IOTA”
(I/Q signals, power management, acoustic, SIM, RF control IC)
U7 ” CalpysoLite_G2”
(DSP IC)
U5 ”NCP345”
(Over Voltage Protection IC)
U104”S-8241”
(Charge IC)
U24 SRAM 2Mbit memory
U100 Flash 16Mbit memory

## Slide 4
Function Block Diagram
CPU(G2)
Calypos Lite
IOTA
PA
CX77324
T/R SWITCH
LMSP43AA-191
Display
Mono B/W
INTEL
Flash
16Mbit
Crystal
A[1..22]
DB[0..15]
Keypad
BSP
USP
Rx_IQ
or
TX_IQ
3Wire
(RF_DAT, RF_CLK, RF_LE)
TI
RITA
26MHz
26’MHz
26’MHz
MIC
Buzzer
SAW
SAW
GSM_Tx
nReset
nCS0
Battery
Conn_3P
BATTEMP
Backlight_LED
Keypad Light
EGSM_Rx (GSM850)
DCS_Rx (PCS)
GSM_PA
DCS_Tx
DCS_PA
Headset
S-8241
APC
APC
NCP345
Voice
AFC
SCLK
SDA
6 pcs
2 pcs
Ear_Detect
TEMP_SEN
TEMP_SEN
PAENA
PAENA
Att_2dB
Att_2dB
GSM_TXEN
GSM_TXEN
GSM_TXEN
GPIO
Receiver
ADC
32KHz
SIM
SIM I/O
Li
Battery
Charger In
nSCS0
Vibration
SRAM
2Mbit
nCS1

## Slide 5
PCB Bottom View
LCM
Microphone
Receiver
D4
LED
D6
LED
D7
LED
D5
LED
D9
LED
D8
LED

## Slide 6
PCB Top View
U14
26MHz Crystal
U15
Tranceiver IC
U1
Power management IC
CON1
SIM connector
J5
Audio jack
BZ1
Buzzer
J13
DC jack
M1
Vibra motor
connector
J1
Battery
connector
U100
Flash IC
U24
SRAM IC
U7
Calpysolite_G2 IC
U13
PA IC
U17
T/R switch
JP1
Mechanical
Antenna Connector
TP43
Internal Antenna
Connector
F2/F3
SAW filter
U6
32.768kHz
crystal

## Slide 7
Power Tree
B+
IOTA
VRDBB
1.5V
120mA
VRRAM
2.8V
50mA
VRMEM
2.8V
60mA
VRIO
2.8V
100mA
VRSIM
1.8/2.9V
10mA
PA
RITA
Regulator
1~3
battery
voltage
supply
Buzzer
Flash
16Mbit
SRAM
2Mbit
CalpysoLite
G2
SIM
CARD
CalpysoLite
G2
LCM
RITA
Serial
Interface
supply
voltage
Analog
Switch
Vibrator
Keypad
light
and
LCM
Back
light
VRF
2.8V
60mA
BJT
for
T/R switch
control