## Slide 1
HEADLINE
C115 RF Trouble Shooting
Present by Allan_Hu

## Slide 2
Agenda
COMPAL COMMUNICATIONS, INC.
RF Tranceiver Block Diagram
Tx Path (I/Q)
Tx Path(LO)
Tx path(PA)
Tx path(TR switch)

## Slide 3
COMPAL COMMUNICATIONS, INC.
RF Tranceiver Block Diagram
PLL
Transmit Path
Receiver Path

## Slide 4
COMPAL COMMUNICATIONS, INC.
Tx Path (I/Q) in GSM Band
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH62:902.4MHz, cell power:-60dBm, MS_TX_level : 5
3. Use oscilloscope probe to touch red point and you can find that(For Example:The TXIP signal)
Probe Point

## Slide 5
COMPAL COMMUNICATIONS, INC.
Tx Path (I/Q) in DCS Band
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH699:1747.6MHz, cell power:-60dBm, MS_TX_level : 0
3.Use oscilloscope probe to touch red point and you can find wave(For Example:The TXIP signal)
Probe Point

## Slide 6
COMPAL COMMUNICATIONS, INC.
Tx Path(LO) in GSM Band
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH62:902.4MHz(CH699:1747.6MHz), cell power:-60dBm, MS_TX_level : 5(0)
2.TX signal1 : Use spectrum probe to touch red point ~ 5dBm (CH=62_902.4MHz, RBW=VBW=200KHz, attenuation=20dB )
3.TX signal1 : Use spectrum probe to touch red point ~ 3dBm (CH=699_1747.6MHz, RBW=VBW=200KHz, attenuation=20dB )
Probe Point

## Slide 7
COMPAL COMMUNICATIONS, INC.
Tx path(PA) in GSM Band
Signal1(APC Wave)
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH62:902.4MHz, cell power:-60dBm, MS_TX_level:5
3.TX signal1 : Use oscilloscope probe to touch R66 to get signal1 wave

## Slide 8
COMPAL COMMUNICATIONS, INC.
Tx path(PA) in DCS Band
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH699:1747.6MHz, cell power:-60dBm, MS_TX_level : 0
2.TX signal1 : Use oscilloscope probe to touch R66 to get signal1 wave
signal1

## Slide 9
COMPAL COMMUNICATIONS, INC.
Tx path(TR switch) in GSM Band
Signal1
VC2
APC
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH62:902.4MHz, cell power:-60dBm, MS_TX_level : 5
2.TX signal1 : Use oscilloscope probe to touch U17 Pin8(R83) to get signal1 wave

## Slide 10
COMPAL COMMUNICATIONS, INC.
COMPAL COMMUNICATIONS, INC.
Tx path(TR switch) in DCS Band
Signal1
VC2
APC
1.Set HP8960 or HP8922,Operating mode:Test mode,Test function:BCH+TCH
CH699:1747.6MHz, cell power:-60dBm, MS_TX_level : 0
2.TX signal1 : Use oscilloscope probe to touch U17 Pin5(R85) to get signal1 wave