## Slide 1
Agenda
A. The mobile phone can’t boot after inserting the Battery
B. SIM unavailable when insert SIM after turn on
C. Display no response after turn on
D. Keypad’s and LCM backlight no response
E. Receiver has no key tone
F. No ring tone
G. Main battery Can not be charging
H. Keypad no function
I. Vibrator out of control
J. Microphone no function
K. Earphone no function
L. Can not record Time
M. Can not Charging

## Slide 2
1. Check energy of the battery.(VBAT>3.8V)
2. Check Battery connector J1
A. The mobile phone can’t boot after inserting the battery(1/2)

## Slide 3
A. The mobile phone can’t boot after inserting the battery(2/2)
3. Check the Power-ON path.

## Slide 4
B. SIM unavailable when insert SIM after turn on
1. If the SIM card in other cellphone.
2. Check the SIM connecter(con1).

## Slide 5
C. Display no response after turn on
1.Check the pad between M/B and LCM’s FPC
2. Check the LCM in other cell-phone.
3. If VRIO_2.8V =2.8V (if VRIO_2.8V <2.7V, the LCD will not work)

## Slide 6
D. Keypad’s and LCM backlight no response
1. Check the LED D4~D11
2. KEYLED_EN= 1.4 ~ 2.8V

## Slide 7
E. Receiver has no key tone
1. If the receiver’s pins slanting or sag->To adjust the Receiver pin
2. Measure the receiver’s impedance(about 32 ohm)
3. M/B pad oxidation or dirty
4. Check the components’ connection and impedance(R1).
5. change a new IOTA.

## Slide 8
F. No ring tone
1.Check the cellphone setting.
2.Check the buzzer connection.
3. Check the speaker’s impedance(about ?ohm).
4. Check the G2 PWT/BU pin(TP1)

## Slide 9
G. Main battery Can not be charging(1/2)
1. Check if you use the right adaptor
2. Check I/O Connector(J13) focus on Pin1 and Pin2.

## Slide 10
G. Main battery Can not be charging(2/2)
1. Check the component’s connection and electric characteristic.
2. Check the Fuse(PT1)

## Slide 11
H. Keypad no function
1. If the connector is oxidized or dirty->Use a eraser to clean the pad
3. Check the ROW and COL
U7 CalpysoLite

## Slide 12
I. Vibrator out of control
1. Check the setting. 2. Check the vibrator’s connection
3. Check the vibrator
4. Is the M/B’s pad oxidized or dirty->Use a eraser to clean the
M/B’s pad. 5. Check the component’s connection.
6. Check BQ1.3 (normal > 3.4V)

## Slide 13
J. Microphone no function
1. Check the microphone’s impedance(?K ohm)
2. Is the M/B’s pad oxidized or dirty->Use a eraser to clean the
M/B’s pad.
3. Check the component’s connection

## Slide 14
K. Earphone no function
1.Check the earphone’s impedance, if it inaccuracy ->replace a earphone
2. Check the earphone’s Jack and connection.

## Slide 15
L. Can not record Time
1. TP46=32.768K, else->change a new U6
U7-G2

## Slide 16
M. Can not Charging:
1.Check you use the adaptor
2.Check I/O Connector failure?
3.Check I/O Connector Pin3&Pin4 solder creak?
4.IF 4.1.if step1 is ok, then change a new IOTA.

## Slide 17
Download Function