## Slide 1: Push-To-Talk
Basic definitions of PTT & How to use PTT on Motorola phones

## Slide 2: What is PTT ?
Push-To-Talk (PTT) is a two-way communication service that works like a "walkie talkie"
PTT functions as a Voice Over IP over GSM phones. i.e. a technology of transmitting voice as data packets over the air

## Slide 3: Continue…
A normal cell phone call is full-duplex, meaning both parties can hear each other at the same time. PTT is half-duplex, meaning communication can only travel in one direction at any given moment.

## Slide 4: Continue…
“Walkie Talkie” serves for a few hundred meters. Since PTT is over GSM it’s coverage is extensible to GSM network coverage

## Slide 5: Continue…
Combining aspects of cellular mobile communications, presence detection, and walkie-talkie style communications, push to talk provides end-users with the ability to quickly find one another and engage in brief, burst-oriented style communication

## Slide 6: Advantages of PTT
Simple Voice Communication
Online Contact Management
One Number Service
Cost Savings

## Slide 7: Simple Voice Communication
With the push of a button, your employees can use Push to Talk for quick exchanges to their co-workers, associates and clients. Connect a buddy or buddies at the touch of a button

## Slide 8: Online Contact Management
Store up-to as many as 200 Contacts
Store up-to 50 group contacts
Edit your contacts Online

## Slide 9: One Number Service
One number, one device for Push to Talk and GSM voice calls

## Slide 10: Cost Savings
Greatest benefits that wireless carriers enjoy from PTT is the network cost efficiencies that are realized in at least two ways.
Use of the underlying IP-based network with half-duplex transmissions has the advantage of both requiring less bandwidth (e.g. network and facility savings)
Avoiding interconnection to the PSTN (e.g. savings against interconnection charges).

## Slide 11: How to PTT
A normal cell phone call is full-duplex, meaning both parties can hear each other at the same time. PTT is half-duplex, meaning communication can only travel in one direction at any given moment.

## Slide 12: Continue…
To control which person can speak and be heard, PTT requires the person speaking to press a button while talking and then release it when they are done. The listener then presses their button to respond. This is just like a WT

## Slide 13: Continue…
Similar way is followed for Group talking
Only one member can be talking at an instant. Other members will be listening.

## Slide 14: Moto phones with PTT
San2riniII, Malta, Royale, Kauai, Bintan/Lanai/Tioman

## Slide 15: Enable PTT on Moto
Select CSM from Idle Screen => Select Settings => Select PTT Settings
    Select “PTT Service”
      Set it to “ON”

## Slide 16: Config Moto PTT
Push the PTT Button
Select “PTT MENU” by pressing LSK
Scroll down and select “PTT Setup”
    Select “GPRS Settings”
      Select “APN” and set this to <Network APN>
      Select “User Name” and set this to <Network User Name>
      Select “Password” and set this to <Network Password>

## Slide 17: Continue…
Select “Server Settings”
  Select “Server1” and set this to <PTT Server IP Address>
  Leave “Server2” field empty
  Leave “DNS IP” field empty

## Slide 18: PTT registration
After powering up the phone, it will automatically attempt to register with PTT server, once the phone is attached to GPRS network. If registration with PTT server is successful, PTT Registration Icon (3rd icon from left at the top) will be displayed.

## Slide 19: PTT Application
Power up the phone & PTT is registered
Press PTT button from Idle screen, PTT Menu with the following fields will be displayed
  PTT Contacts
  PTT Groups
  PTT Quick Group
  PTT Setup

## Slide 20: PTT Contacts
This dialog shows the list of Contacts available just like phonebook
Presence status icons will be present in front of the individual contact
Highlighting a contact & the Left soft keys
  ALERT indicates that the CONTACT which is highlighted is online
  REFRESH indicates that the CONTACT which is highlighted is offline

## Slide 21: PTT Groups
This dialog shows the list of Groups available just like phonebook
Presence status icons will be present in front of the individual contact
Highlighting a contact & the Left soft keys
  View indicates that the CONTACT which is highlighted is online
  REFRESH indicates that the CONTACT which is highlighted is offline

## Slide 22: CSM in PTT Appln.
Contacts & Groups CSM has the list of operations that can be performed over a highlighted contact or group
Operations that can be performed over a contacts are
  ADD
  EDIT
  DELETE
  BLOCK
  Online Alert
  View

## Slide 23: Continue…
Operations that can be performed over a Group are
  ADD
  DELETE
  Online Alert
  View

## Slide 24: Operations – How To
ADD
  Press PTT button => PTT Menu => PTT Contacts/Groups => Press the CSM =>Select ADD Enter the NAME and PHONE NUMBER of the contact and press LSK (DONE). This shall add the contact into the CONTACT LIST
  Press PTT button => Press CSM => PTT Groups => CSM=>Create New Group. Select “Name” option to add name for group. Select “Members” to add members to group. Members to group can be only added from list of contacts present in contact list. Press DONE LSK to confirm creation of group.

## Slide 25: Continue…
DELETE
  Press PTT button => PTT Menu => From the PTT CONTACTS list, highlight the contact => Press CSM =>Select DELETE This shall delete the contact from the CONTACT LIST
  Press PTT button => PTT Menu => PTT Groups => select group to be deleted, press CSM, select “Delete” option to delete selected group

## Slide 26: Continue…
EDIT
  Press PTT button => PTT Menu => From the PTT CONTACTS list, highlight the contact => Press CSM =>Select EDIT This allows to change the name of the contact.
  EDIT Group is not supported

## Slide 27: Continue…
BLOCK
  ADD Contact provides the option to Block the contact while creation
  EDIT Contact provides the option to modify Block operation
  Groups cannot be blocked

## Slide 28: Continue…
Online Alert
  This can be set only for a Contact/Group who is offline. For offline contact, press CSM, second item is “Enable Alert to Online”, press “Select” RSK to set online. For setting Online Alert tone, Press PTT button => Press CSM => Scroll down and select “PTT Setup” => Select “PTT Personalize” =>Select “Set Online Alert Tone” to either ON or OFF.

## Slide 29: Continue…
View Contact
  Press PTT button => PTT Menu => PTT Contacts => select a contact =>Press CSM=>Select VIEW This displays phone number/Online alert status & Block/Unblock status Online alert indicates that whenever a particular contact becomes online, depending on online alert tone settings, corresponding tone will be played.

## Slide 30: Continue…
View Group
  Press PTT button => PTT Menu => PTT Groups => select a group =>Press CSM=>Select VIEW This displays Group name/Online alert status & Online alert indicates that whenever a particular contact becomes online, depending on online alert tone settings, corresponding tone will be played

## Slide 31: Frequently Used
Press CSM from PTT Contacts/Groups select “Frequently Used” option, this will result in contacts and groups being sorted based on the number of times PTT calls have been made to a particular contact. The contact to which most PTT calls made shall be at the top of the list

## Slide 32: Refresh list
Press CSM from PTT Contacts/Groups =>Select REFRESH LIST This shall update the status (ONLINE/OFFLINE) of the contacts in the Contacts/Groups LIST

## Slide 33: PTT Calling
PTT calling is similar to voice calling
Instead of SEND key dedicated PTT key has to be pressed
Highlight a PTT Contact or group & pressing PTT button will make a PTT call

## Slide 34: PTT Alert
Highlight a contact in the Contact list & see the RSK as ALERT if the contact is online
Pressing ALERT Alerts the user at the other end like the initiator wants to talk
There is no Auto-Accept for PTT Alert. The user always gets an Alert dialog irrespective of the PTT personalize settings

## Slide 35: How To- One-2- One Call
  PTT call Initiating side: Push the PTT Button => From the PTT CONTACTS list, scroll down to the Contact to which the PTT call is to be made => Press the RSK (ALERT) or PTT button.
  PTT call Receiving side: The Contact will receive an alert. Upon pressing the RSK (ANSWER), the PTT call gets connected.

## Slide 36: Continue…
Now, either of the contact can take the floor (TALK) by pressing and holding the PTT button while they are talking. When the PTT button is pressed while still in the LISTENING mode, a beep sound is played which indicates that the FLOOR (Other side is still talking) is still taken by other side.

## Slide 37: How To- PTT Group Call
Two kinds of Group Calls
Instant Group Call
  Press PTT button => Press CSM => Scroll down and select “PTT Groups” =>Highlight a Group =>Press the PTT button
  On the receiving side, the Contact will receive an alert. Upon pressing the RSK (ANSWER), the PTT call gets connected.

## Slide 38: Continue…
Quick/Adhoc Group Calls
  Go to PTT Contacts => Press CSM => select Quick Group => randomly select desired PTT Contacts => press PTT button
  On the receiving side, the Contact will receive an alert. Upon pressing the RSK (ANSWER), the PTT call gets connected.

## Slide 39: Continue… (Group Calls)
When all the users accept the call, the call is connected. Any user can take the FLOOR (talk) and the rest of the users shall hear the voice. Any user can disconnect from the group call by pressing RSK (EXIT). When the PTT group call initiator presses RSK (EXIT) or the END button, the group call ends.

## Slide 40: Continue….
PTT Individual Calls can be made from
  Phonebook
  Recent calls
  Notepad
  Number entry from idle screen
  And also from the PTT Contacts
Instant Group Calls can be made only from PTT Groups
Quick Group calls can be made only from PTT Contacts

## Slide 41: PTT on CLI
Pressing PTT button on CLI will launch PTT Application
PTT Individual & Instant Group Call can be made by pressing against the contact displayed in the CLI by pressing PTT button again
Quick Group Call cannot be made from CLI
Clamshell open & close does not ends a PTT Call

## Slide 42: PTT In-Call
Set SPEAKER to ON/OFF during a PTT call
  While the PTT call is connected, press the RSK (SPEAKER) to change the Speaker functionality to ON/OFF
END Call
  While the PTT call is connected, pressing the END key or EXIT LSK shall end the PTT call

## Slide 43: PTT Personalize
Press PTT button => PTT Menu => PTT Setup => Select “PTT Personalize”
Options
  OPEN TO
  SORT BY
  MY ANSWER MODE
  Tone Volume
  PTT SPEAKER
  Online Alert Tone

## Slide 44: “Open To” Options
Pressing PTT button from idle screen with the following options:
Contacts
  Displays “PTT Contacts”
Last Called Contact
  Displays “PTT Contacts” with last called contact on the top of the list
PTT Menu
  PTT Main Menu will be displayed

## Slide 45: “Sort by” Options
PTT Contacts or Groups gets sorted based on the following options
Name
  Contacts are sorted by alphabetical order
Status
  Contacts are sorted based on the online status
Frequency
  Contacts are sorted based on frequency of calling.

## Slide 46: “MY ANSWER MODE” Options
Behavior of phone for an incoming PTT call.
Manual
  Incoming PTT call dialog with soft keys Ignore & Answer will be displayed.
Auto Accept
  Incoming PTT call gets connected automatically after a beep tone.
DO NOT DISTURB
  This option ignores any kind of PTT call made to the Phone

## Slide 47: Tone Volume
This option displays a volume slider with a threshold ranging from 1 to 7
This option is similar to the volume slider in a voice call
The value set in this option controls the volume level during a PTT call
Side volume keys can be used to increase & decrease levels during a PTT Call

## Slide 48: “PTT Speaker” Options
The value will default the Speaker to either ON or OFF when a PTT call is connected
  ON – The speaker shall be set to ON when a PTT call is connected
  OFF – The speaker shall be set to OFF when a PTT call is connected

## Slide 49: “Online Alert Tone” Options
On
  Plays tone when Online Alert is enabled for a contact or group & the contact comes online
Off
  Doesn’t plays tone when Online Alert is enabled

## Slide 50: PTT Button Lock
Idle screen => CSM => settings => security => Select “Lock PTT Key”
Setting this option to ON shall disable the PTT button when the flip is closed thereby reducing the chance of any accidental PTT call initiation to other contacts. This functionality will become active after 1 minute (flexible) once flip is closed
Setting this option to OFF shall enable the PTT button at all times. PTT calls can be made with the flip closed.

## Slide 51: Continue…
Button Lock is not available for Candy bar phones
Keypad lock locks the PTT button

## Slide 52: PTT Icons

## Slide 53: Continued…

## Slide 54: Continued…

## Slide 55: PTT Sounds

## Slide 56: Continued…

## Slide 57: PTT Flexing
Every product release notes has a unique flex for PTT.
E.g.: GITSAN2200PTT01E.hs
GITSAN2200AA01E.hs
GM flex is common for non PTT & PTT phones
In GI- PTT flex file PTT is enabled
To flex off PTT standard GI flex can be used in which PTT is flexed off

## Slide 58: SIM Provisioning
To enable PTT SIM Card must be provisioned with the PTT Server. i.e. a new account has to be created in the PTT server with the SIM – MSISDN number. With this account you can access your Contact & Group list in the remote server.

## Slide 59: References
Marketing Requirement specification#9336
Push-To-Talk over the Cellular (PoC) Functionality
Ver#0.9

## Slide 60: Further Details
More details of
PTT Application
HW configuration
Flexing info
SIM provisioning & FAQ
please refer
http://compass.mot.com/go/mmiptt30

## Slide 61
Thank You