## Slide 1
MOTORAZR V3
V3_06

## Slide 2
Specifications
SA Date: Q2 2007
Form Factor: Clam Shell
Antenna: Internal
Bands/Modes: GSM 850/900/1800/1900 MHz, GPRS/EDGE Class 10
(2U/4D)
Weight: ~ 95g
Dimensions: 53 x 98 x 13.9mm
Display: 2.2”, 176 x 220, 262k Color TFT, Main Display
1.0”, 96 x 80, 65k Color CSTN, CLI Display
Battery: 710mAh Li-lon (BR50, SNN5696)
TT/SB Time: up to 6 – 8hrs of TT
up to 6.5 – 10.4 days of SBT
Memory: 32MB Flash x 8MB PSRAM
(4.5M User Memory, but depends on customer SW loading)

## Slide 3
Messaging: MMS, SMS, EMS, IM (Wireless Village), E-Mail (POP3,
SMTP, IMAP4)
Audio: 22 KHz polyphonic speaker
Video : MPEG4 & H.263 (Record & Playback), 3D Graphic Engine
Music: MP3, MIDI (24 channel)
Imager : VGA, 4x Digital Zoom, Fixed Focus
Connectivity: EMU, Bluetooth Class 2, USB
Browser: WAP2.0, MIDP2.0, J2ME
Key BL: Blue EL Light
Key Features & Enablers

## Slide 4
Key Selling Point
RAZR ID (Ultra thin design)
Brilliant 2.2”, 262K TFT color display & 64K CSTN external display
Dynamic Idle (carrier dependent)
Picture caller ID on both displays (Allows you to see who’s calling)
Dedicated Message Center & Browser keys
Bluetooth® Connectivity (Class 2, up to 30 feet)
Multi-letter phonebook search
Integrated Speakerphone

## Slide 7
** Neptune LTE2 & AUL are common

## Slide 8
CMF base on Razr 05, PCB layout base on Siliqua EDGE

## Slide 20
Visual differences between RAZR05 and RAZR06

## Slide 21
Main PCB
memory
Neptune LTE2
MIC
transceiver
Bluetooth
26MHz
Crystal
for BT
26MHz
Crystal
for U250
PA
Atlas Ultra Lite
32.768KHz
Crystal
EMU Conn
Vibrator
SIM Conn
Battery Contact
Main-to-Flip Flex Conn

## Slide 22
Flip Flex Circuit
earpiece
Backup Cell
Main Display Flex Conn
Graphic Accelerator
Camera Module Socket
Flip-to-Main- Flex Conn
LED Driver
CLI Display Flex Conn
Side Buttons

## Slide 23
Manual Test Commands
To enter test mode :
Press “Menu” button followed by 048263*
To enter suspend mode :
Enter “54”, then select <OK>
When “Success” message appears, select <Back> to activate
Other testing commands are same as V3 series families

## Slide 24
Block Diagram