## Slide 1: E770v/E3 ROKR RF Troubleshooting

## Slide 2: General tips
Make sure equipment is calibrated
Duplicate Gate system failure on the tech bench. Use same test parameters as Gate system
Try different mode and bands (Example : Test mode and on call)
Try to differentiate between Gate system issues and component failures.
If you can not duplicate the issue on your bench, always work with test engineers for further analysis method.

## Slide 3: Troubleshooting setup

## Slide 4: GSM RX Equipment Setup
Test Equipment
  Setup to non-signaling mode
    CMU 200 – P/t Normal GMSK
    R&S 8960 – GSM BCH
  BCH: 700(DCS)
  Level: -30dBm
Phone under test
  Send PC commands (Radiocomm)
    CP_MODE: 900/1800
    SCMP: 700

## Slide 5: GSM RX Line-up
FEM
Blue
Module
Balun
Harmony
POG
RX Carrier
RX IQ
BDR

## Slide 6: GSM RX Troubleshooting
Failing BER (Bit Error Rate)
  Check RX line-up
    FEM (Ant in, RX out, control lines)
    Balun (In, Out)
    Blue Module (RX in, RX IQ)
  If RX Line-up ok, check RSSI
    Pass
      POG issue. Replace POG
    Fail
      Harmony Issue. Replace Harmony

## Slide 7: GSM TX Equipment Setup
Test Equipment
  Setup to non-signaling mode
    CMU 200 – P/t Normal GMSK
    R&S 8960 – GSM BCH-TCH
  TCH: 512(DCS)
Phone under test
  Send PC commands (Radiocomm)
    CP_MODE: 900/1800
    SET_RF_PWR: 10
    Channel: 512
    CARRIER: Option 00, ON

## Slide 8: GSM TX Line-up
FEM
Blue
Module
PA
POG
TX Carrier
BDX
(No Test points)

## Slide 9: GSM TX Troubleshooting
TX failure
  Check current : It should draw about 500-600mA.
  GSM TX work but DCS/PCS doesn’t work or vice versa
    Defective PA. Replace PA
  Not enough output power at maximum power step
    Check Maximum output power when it is saturated. Should show at least 1dB higher than target power.

## Slide 10: GSM Troubleshooting
TX failure
  Check current : It should draw about 500-600mA.
  GSM TX work but DCS/PCS doesn’t work or vice versa
    Defective PA. Replace PA
  Not enough output power at maximum power step
    Check Maximum output power when it is saturated. Should show at least 1dB higher than target power.
RX Failure
  Check simple camp using ToolBox. Compare between input RF level and reported RF level from phone.
  Access point between FEM to Blue module : expect to see RF frequency.
  Access point between Blue to Harmony : when input at antenna is -50 to -40, expected Vac,pp : 2.5-3.5V

## Slide 11: WCDMA RX Equipment Setup
Test Equipment
  Setup to non-signaling mode
    CMU 200 – Receiver, BER
    R&S 8960 – FDD
  Downlink Channel: 10700
    To read RX IQ, offset freq by 1 kHz
  Level: -30dBm
Phone under test
  Send PC commands (Radiocomm)
    CP_MODE: W2100
    WSCMP: 10700 (06 response = Success)

## Slide 12: WCDMA RX Line-up
FEM
Blue
Module
LNA
Harmony
POG
RX Carrier
RX IQ
BBIF RX
(No Test points)

## Slide 13: WCDMA Troubleshooting
RX failure
  Run WCDMA RSSI test
  There are 6 test points right next to Harmony. When those voltage present, GSM and WCDMA most likely working fine. If any of those voltages not present, RX path is not working properly.
    TP516-519 WB_DCOC_I/Q : 1.8Vdc
    TP509, TP510 : MBC_EN_1/2 WCDMA LNA enable and low/high gain mode switch 2.775Vdc

## Slide 14: WCDMA TX Equipment Setup
Test Equipment
  Setup to non-signaling mode
    CMU 200 – Transmitter, Max Power
    R&S 8960 – FDD
  Uplink Channel: 9750
Phone under test
  Send PC commands (Radiocomm)
    CP_MODE: W2100
    W_CARRIER: 9750, Enable,

## Slide 15: WCDMA TX Line-up
FEM
Rattler
PA
Harmony
POG
TX Carrier
TX IQ
BBIF RX
(No Test points)

## Slide 16: WCDMA Troubleshooting
TX failure
  Test TX output power on test mode
    Current for requested power 21dBm : 700-900mA
    If not enough current present, check RF signal between Rattler and WCDMA PA. Expected to see same frequency as TX frequency. If the RF signal does not present, check I/Q line from Harmony.