## Slide 1
Z9
WDCMA 850/1900 –
GSM Q-Band Edge

## Slide 2
V9 US
Z9 US
Memory
Display
Antenna
Connectivity
Alert Speaker
Others
RF
Baseband Chipsets
Camera
GSM/Edge Tranceiver IC “TRANSAAM”
WCDMA Tranceiver IC “SYMPHONY”
Atlas V3,5
Micro USB
Linear Vibrator (in Flip Hinge )
Navigation keypad
Main 2,2“Color 262K,CLI 2,0” Color 262K
2,0 Mega pixel Main Housing mounted
3 x 14 x 20mm Dynamic Speaker
Same
Same
Same
Same
Same
Same
Same
GSM/Edge/WCDMA Internal Antenna 850, 900, 1800,1900
Same
Same
10 x 16mm oval Polyphonic Speaker
SIM + T-Flash Cardreader
Main 2,4“Color 262K
Linear Vibrator (in Keypad flex)
Z9 US vs. V9 US
GSM/Edge – “ORPHEE”, WCDMA “Passkey”
AGRON LV
Graphics Processor + Serializer
64MB NOR / 64MB NAND / 64 MB SDRAM
Same
Same

## Slide 3: Top Side
J2300
Hydra-Flex
Connector
U1000+POP
Argon LV+ Argon Memory
BB Processor
U100
Symphony
WCDMA
Tranceiver
U400
1900 Mhz
Passkey
U450
850 Mhz
Passkey
U6000
GPS Receiver
U300
1900 MHz
LNA
U350
850MHz
LNA
J3
Camera
Connector
J2
Keypad
Connector
BT1
Coincell

## Slide 4: Bottom Side
M5500
USIM
Connector
J5801
T-Flash
Cardreader
J5400
Battery Connector
M001
Mechanical
Antenna Switch
U001
FEM
(below Shield)
U800
GSM PA
J6000
GPS Antenna
Connector
U3000
Atlas
U5600
BlueTooth
J5000
Micro USB
Connector
U5201
Graphic Data
Serializer
U5200
Graphics Processor
U500
TRANSAAM
GSM/ EDGE
Tranceiver

## Slide 5
Main Chipsets
U001 Front End Module
(Duplexer, Antenna Switch)
U100 WCDMA Transceiver
(Mixer, IF, VCO´s , Exciter, BaseBand
U300+U350 WCDMA LNA`s
  (Low Noise Amplifier, Splitter, Filter)
U400+U450 WCDMA PA`s
(PA, Splitter, Filter)
U500 GSM/EDGE Transceiver IC
  (LNA, Mixer, IF, VCO´s , Exciter, Synthesizer ,Control, B-Band)
U800 GSM PA - Low/High Band
  (Low and High Band PA, Filter)
U1000 Argon LV
(BB Processor, DSP, )
U1300 Argon POP Monolithic Memory
(64MB NOR, 64MB NAND, 64MB SDRAM)

## Slide 6
U3000 “Atlas 3.5”
(Audio Stereo ,Power Supl., over Voltage interface, Charger interface, Backlight Sink circuit, USB 1.1 interface)
U5200 Graphics Processor
( Display and Camera Controller)
U5201 Serializer
(Parallel to Serial Data interface for Display Data)
U5600 Bluetooth
(Class II Bluetooth Transceiver)
U6000 GPS Module
(GPS Receiver with external LNA and Reference Clock)
Main Chipsets

## Slide 7: U001
Front End Module (FEM)+mechanical Antenna Switch
Max 4 Band GSM, 2 Band WCDMA antenna switch with integrated diplexer.
Used in all model variations of Z9 (850/1900 WCDMA)
Mechanical Antenna Switch
Low Band Antenna Switch
Diplexer
High Band Antenna Switch
Control Interface Signals
Truth Table FE1–FE2-FE3

## Slide 8: U100
Symphony
WCDMA tri-band exciter (TX) and receiver back-end for UMTS Band 1,2 and 6, 165 pin BGA
High Band Receiver - Mixer, AGC, IF, Filter..to BB
Low Band Receiver – Mixer, AGC, IF, Filter..to BB
RX VCO
TX Low Band Exciter
PLL and Charge Pump
TX VCO
Reference Clock Control Interface
TX Low Band Mixer
TX High Band Exciter
TX High Band Mixer
TX Modulation/ Data Setup
TX PA Power Control and Sequence Manager

## Slide 9: U300 + U350
LNA with Bypass
Band Pass Filter
Splitter
2nd LNA
WCDMA output
GSM output
Circuit Enable Signal
Gain Enable/Disable
WCDMA High and Low Band LNA
Low Noise Amplifier, Splitter, Filter two low-noise amplifiers (LNAs), one 3 dB splitter, one band-pass filter,
one logic gate for LNA mode control, and biasing, matching, and attenuator circuitry.
U320:
WCDMA High Gain Mode ~ + 20dB
WCDMA Bypass mode ~ -3,5dB
GSM Mode ~ +9,5dB
GSM standby Mode ~ -20dB
U350:
WCDMA High Gain Mode ~ + 18dB
WCDMA Bypass mode ~ -3,5dB
GSM Mode ~ +9,5dB
GSM standby Mode ~ -20dB

## Slide 10: U400
The Passkey-4W is a single Band module that integrates an inter-stage filter, power amplifier, coupler,
power detector, and duplex filter for the 1900 MHz Band. The circuit is designed for undervoltage,
temperature, and load VSWR conditions.
Duplex Filter
Power Detector
Power Amplifier
Inter-Stage Filter
WCDMA PA – High Band

## Slide 11: U450
The Passkey-1W is a single-band, WCDMA PA module. The module integrates an inter-stage filter, power amplifier,
coupler, power detector and duplex filter for the 800MHz Band. The circuit is designed for under voltage,
temperature and VSWR (Voltage Standing Wave Ratio) conditions
Duplex Filter
Power Detector
Power Amplifier
Inter-Stage Filter
WCDMA PA – Low Band

## Slide 12
U500
RX Front End with LNA´s + Mixer
Very Low IF (122,7 KHz)
RX /TX Baseband Interface
Fractional-N Synthesizer
TX Power Amplifier (Exciter)
RX VCO /TX VCO
TX Modulator
Control Interface
Power Interface
GSM Tranceiver Circuit „TransAAM“
Quad band GSM/EDGE transceiver solution consisting of Fractional-N synthesizer, VLIF (122,7kHz) RX front end,
GSM/EDGE TX modulator, power amplifier control circuitry, auto calibration functions, signal processing and auto
sequencing functions. The TX modulator functions are completely contained within the module.
The RX circuitry includes all circuitry required to convert RF inputs into digital I and Q signals. The baseband interface
consists of a serial control and serial data configuration that can function in both full DigRF and Neptune compatible
modes. The module requires the Raptor or Ophee PA and Saw filters to complete the RF solution.
Notes: <number>
<footer>
<header>
<date/time>
High-level chipset partitioning
Chipset walk-through

## Slide 13
U800
GSM PA – Low/ High Band
The Orphee module is a input/output, quad-band, dual-mode, GMSK/8PSK(EDGE) PA module
intended for 2.75G radio applications. The module consists of a dual line-up power amplifier, harmonic
filter, logarithmic power detector, and analog power control circuit. This PA module is used in the final
amplification stages in a GSM portable telephone operating in either GMSK or EDGE mode.
· EDGE Class 12 operation
· GMSK power class 4 operation in the GSM850 and EGSM900 bands
· GMSK power class 1 operation in the DCS1800 and PCS1900 bands
· EDGE power class E2 operaton
Harmonic Filter
Power Detector
3-Stage PA Low /High Band
Low Band /High Band selection
Input or Bias control mode selection
Transmit Enable
Analog PA Bias Control signal
Power detect feedback

## Slide 14
The ArgonLV POP IC is a multi-standard baseband IC with included application, covering wireless standards such as W_CDMA, GSM, GPRS, and EDGE. Argon+ combines the StartCore-SC140v3 DSP subsystem to execute the Layer-1 modem functions for very high downstream data rates, and the ARM11 subsystem for executing Layer 2&3 modemfunctions as well as running demanding applications such as video decoding or video telephony enabled by graphics and video accelerators. A large number of serial and smart card interfaces are integrated on the IC to guarantee high versatility. The memory interface has been designed to support most of the available and announced future volatile and non-volatile memory devices. This IC is housed in a 604 pin, 15x15 x 0.9 mm POP BGA package with 0.5 mm pitch.
Argon LV Baseband Processor
• ARM11 running at 399MHz
• StarCore SC140 running at 208MHz
• SDMA for improved inter-processors communication running at 133MHz
• External Memory IF, SDR/DDR SDRAM running at 133MHz
• WAMMO to support 3GPP Release 5 (HSDPA) running at 16x chip rate
(61.44 MHz).
• E-fuse support
U1000

## Slide 15
ARGON Internal Block
U1000

## Slide 16: SC140 (DSP) platform
SC140e
  208MHz (250MHz in turbo mode)
  Interrupt Controller
Cache
  32 kB L1 D cache
  16 kB L2 I cache
  128 kB L2 unified cache
  32 kB M1 RAM
On-chip memory
  32 kB M1 RAM
  1 MB M2 ROM
  640 kB M2 RAM
SCMA11 Block

## Slide 17
U1300 POP Memory
Argon POP External Memory
Monolythic Memory, Part on Part Part Design, 64 MB NOR Flash, 64 MB NAND Flash,
64 MB SDRAM.

## Slide 18: U3000
Analog Baseband controller
with following interfaces:
On Logic
Real Time Clock Interface
Power Regulators
GPIO Reset Interface
Inter IC Control Interface
Charger Interface
Control Logic
USB Inter IC Interface
Audio SAP
Backlight Sink Control
USB 1.1 /Audio Interface
The Atlas is designed as Power Control Audio Power IC used in cellular transceivers.
Atlas will handle the audio and power management requirements for the system such like USB, Regulators, Charger Interface, Audio Codec; LED Sink circuit, RTC Interface.
The Circuit is in a 247 pin 0.5mm pitch 10x10 Ball Grid Array (BGA) Package.
Atlas 3.5 Power Control - Audio Power

## Slide 19: Atlas
ATLAS Block overview

## Slide 20: U5200
Graphics Processor
Camera Interface
Power
Clock interface
LCD Interface
High Speed Communication Interface
3,3 Volt Power Supply for USB 2.0
USB 1.1 Interface in Atlas
SC12 Wireless Media Processor with stunning, high performance 3D graphics, TV quality video capture and playback, and digital camera quality for cell phone, PDA, or other powered handheld devices.
With its powerful 128-bit 3D engine, the SC12 includes a dedicated hardware MPEG-4 codec, support for 3 MP still image capture, and the ability to drive a VGA LCD, all from 1280 kB of internal memory.

## Slide 21: U5201
Serializer
Low voltage/ Low current High Speed Serial interface
• LVCMOS I/O interface: 18-bit RGB Interface, 8/16/18-bit CPU Interface
• Dual Power Supplies: Core Supply: 2.5 to 3.0V Parallel I/O Supply 1.6 to 3.0V
• Single device to operate as serializer or deserializer
• Standby Power-Down mode support
• One directional SPI Mode support for CLI Display
• Package: 42uBGA 3.5mm x 4.5mm with 0.5mm Ball Grid Pitch
Power Supply Interface
Clock Interface
High Speed Serial Interface
Logic Control Interface

## Slide 22: U5600
Bluetooth Class 2.0
The U5600 is composed of a Bluetooth V2.0 compliant host/controller and complementary RF circuitry to be utilized in GSM and WCDMA cellular applications. The host/controller interface is designed to be a 4 wire UART connection. A digital Audio Interface (ASAP) is used to intercommunicate to the BB Processor.
Digital Audio Interface
UART host/ controller
Clock Interface
RF Interface
Logic Control Interface

## Slide 23: U6000
GPS Receiver
The U6000 is a standalone integrated GPS (Global Positioning System) receiver packaged. The package consists of a custom digital processor, and a custom RF receiver.
The RF receiver includes an LNA, fractional-N synthesizer with integrated VCO, integrated IF filter,
AGC circuitry and a serial port interface. The digital processor consists of a GPS acquisition engine with 32,768 correlators, high-speed SRAM, an instruction ROM, ARM7S processor and dual UART interface.
This part has a -30 °C to +75 °C operating temperature range, and is intended for use in handheld devices.
GSCI5000 receives & decodes GPS signals at 1575.42 MHz. It is a self-contained GPS receiver capable
of producing a final position solution including full tracking and data decode capability. The hardware
architecture supports assisted and autonomous operation but all tracking functions for autonomous
operation must be in software and fit within the 2 Mbit ROM memory.
Frontend with external LNA
GPS Receiver
UART host/ controller
Power Interface
Clock Interface

## Slide 24: Charger
Charge Control Interface
Battery Connector
Dual Charge Transistor
Curret Sense Resistor
Battery to B+ Switch
VBUS to B+ Switch
Micro USB Connector
Charger

## Slide 25: Clock Tree
Symphony
GPS
Transaam
Argon
GPU
2M Camera
26MHz
26MHz
15.36 MHz
26 MHz
TCXO
Y190
U100
U6000
U500
U5600
Atlas
U3000
U1000
XCLK
REF_CLK_IN
REF_CLK
U5200
CLIA
WB_REF_CLK_IN
PCLK
Display
Flip
Syn_CLK_out_0
Syn_Ref_In
GSM_TCXO
Syn_CLK_out_2
Syn_VCO_CLK_out
SIM
SIM1_CLK0
R28
E13
Syn_XTAL_CLK_out
F14
R24
CKIH_REF_CLK_IN
H15
26MHz
XTAL2
XTAL1
XTAL
Y3986
32.768 kHz
V16
V14
T-Flash
J5001
5
L6
1
4
M
H
z
AD8
MMC1_CLK
1
A23
M5500
20-25 MHz
3.25 MHz
VCLK
B14
AG23
CK01
Serializer
DISP_MCLK
FSCLK
DispCLK+
285 MHz
78 MHz?
36 MHz?
DispCLK-
1
2
M
H
z
FLCLK1
APPS_CLK
Flip CONN
26 MHz
A9
VGPO
C9
U5201
D1
E1
STRB1_WCLK1
B4
E14
F1
OSCFO
G15
F13
CLK32K
R14
LOW_REF_CLK1
D1
PERIPH_32K_CLK
CKIL
A21
32 KHz
32 KHz
Syn_CLK_out_1
26MHz
2.71 MHz
WB_CKIH_CLK
ARGON_REF_CLK
USIM_CLK
SD1_CLK
GPS_CLK
F13
REF_CLK
S
Y
N
R
E
F
I
N
G
S
M
T
C
X
O
Bluetooth
32 KHz
10