## Slide 1
E8

## Slide 2
Generic Overview
Market Name: E8
Manufacturer: Motorola
Form Factor: Candy Bar
Bands/Modes: GSM Quad Band 850/ 900/ 1800/ 1900MHz
Memory Internal: 128MB Flash, 64 MB SDRAM, 2GB embedded MMC user memory
Memory External: up to 4GB –Micro SD
Expected SA Date : Oct 2007
Displays: 2.0” QVGA 240x320, 262K color TFT
Antenna: Internal
TT/SB Time: BK60, 970mAh Battery - TT up to 360min, SBT up to 300 hours
Customer Sync. SW: Mobile Phone Tools
Available at: Customer Stores

## Slide 3
E8
U9
Memory- internal -
Memory external -
Display
Antenna
Connectivity
Alert Speaker
Others
RF
Baseband Chipsets
Camera
GSM/Edge Tranceiver IC “TRANSAAM”
PA “RAPTOR”
SCMA11
Atlas V3,5
- 128MB Flash, 64MB SDRAM, 2GB MMC
- up to 4GB Micro SD
Micro USB
Main 2.0“Color 262K,CLI 1.45” Color 64K
Quad-Band Internal Antenna
2,0 Mega pixel Main Housing mounted
Serializer IC
10 x 16mm oval Polyphonice Speaker
SIM Cardreader
Linux/Java platform product
E8 vs. U9
Linear Vibrator
GSM/Edge Tranceiver IC “TRANSAAM”
PA “RAPTOR”
SCMA11
Atlas V3,5
Micro USB
Navigation Keypad
Main 2.0“Color 262K,CLI 1.45” Color 64K
Quad-Band Internal Antenna
2,0 Mega pixel Main Housing mounted
Serializer IC
10 x 16mm oval Polyphonice Speaker
MegaSIM Cardreader
Linux/Java platform product
Vibrator Motor
USB 2.0
- 128MB Flash, 64MB SDRAM
- up to 4GB Micro SD
USB 1.1
Morphing keypad with Omega scroll sensor

## Slide 4
Daughter PCB
M6
Connector
MK1
Mic.
J11
Ant. Con.
B2B
Antenna wire
Keypad Mylar
EL film
M4, M5
Connector

## Slide 5
Top Side
J1100
T-Flash Con.
J1300
SIM Con.
U400
FM-IC
U300
Bluetooth
J250
JTAG
J2000
Key Con.
U500
USB2.0
J1600
Daughter
PCB Con.
J1800
Disp. Con.
U700
Flash/RAM
J1500
Cam/Headset
(MFT)
J1700
Micro USB

## Slide 6
S1250
Slide Sw.
U900
Atlas
U800
SCMA11
U200
Raptor PA
Bottom Side
U100
TransAAM
M1200
Batt Con.
U750
2GB Memory
FL200
SAW Fl.

## Slide 7
MFT Assembly
2MP
Camera
3,5mm
Headset
Speaker
Side Key‘s.

## Slide 8
Touch Sens.
Touch to Key interface
Front Housing
Haptic Feedback
Piezo Speaker

## Slide 9
Main Chipsets
U200 “PA + Antenna Switch” – (RAPTOR)
  (RX/TX Switch, PA + Matching)
U100 “GSM /EDGE Tranceiver IC” – (TRANSAM)
  (Frontend IC, RX/TX VCO)
U800 “SCMA11”
  (DSP, De/ Modulation, VCO driver, Graphic, Memory Card, Cam)
U700 “Flash”
  (1GB plus 512MB SDRAM)
U750 “Embeded Memory”
  (2GB NAND Memory, User)
U900 “Atlas 3,5”
(Audio Stereo ,Power Supl., over Voltage interface, Charger interface, Backlight Sink circuit, USB interface)
U500 Serializer
(converts the parallel ATI graphic Display Data into serial)
U300 Bluetooth
U400 FM IC

## Slide 10
Main Board
(Transceiver)
Daughter Board
(Daughter)
Daughter Flex
(DFlex)
40 pin
connector
24 pin
connector
PersonalityFlex
(PFlex)
RF Cable
ACF Pads
Interconnection Plan

## Slide 11
Keypad Interface
FSR Membrance Switch
Elba uses the 2-pole keypress detection scheme like all synergy phone models. But the material used for the keypad “dome” is different. It is called a “FSR Membrane Switch”
This material is similar to the ones that are used in most household appliances like Microwave ovens and washing machines.
The drawing below shows the structure of a “FSR Membrane Switch”

## Slide 12
Keypad Interface

## Slide 13
Keypad Interface
Pelikon/Solomon HVIC Solution
Shutter + EL
Shutter 8 Segments
Shutter 1 Backplane
EL 8 Segments
EL 1 Backplane
SCM-A11
2.775V I2C
QT12C02-XSG
SPI1_SS1
3 channels
Touch Sensor
Touch Sensor
1 channel
1 channel Guard Band
Omega Wheel
1.8V I2C
I2CLK
I2DAT
Level Shifter
UH2_RXDP
UH2_PWR
Atlas
GPO2
Reset
RCHG Interrupt
Reset
Playtime Module
Solomon - 32KHz Clock
CLK32K
KCHG Interrupt
UH2_TXOE_B
Pelikon - DBG
GP_SP_A3
5 x 6 Keypad Matrix
KPCOL[0:5]
KPROW[0:4]
UH2_TXOE_B - The signal on Elba is being called TNLC_RCHG. This is the interrupt from the capacitive sensing peripheral that signals the host processor that a user initiated event has occurred on the omega scrolling device
UH2_RXDP - The signal on Elba is being called TNLC_KCHG_INT. This is the interrupt from the capacitive sensing peripheral that signals the host processor that a user-initiated state change has occurred on touch sensor.
UH2_PWR - The signal is being called CAP_RESET on Elba, and is used for resetting the capacitive sensing peripheral.

## Slide 14
Keypad Interface
GP_SP_A3 – SCMA pin name is U3_CTS_B. The signal will be called UI_IC_DBG on Elba. This signal is used for reprogramming the morphing front panel assembly "on the fly" so the phone teams won't have to rework phones or build new ones every time Motorola or the customer wants to change the look and feel of the morphing in some way. This pin is required only for Pelikon solution and not for Solomon solution. This connection is different from R1.
SPI1_SS1 - The signal is being called FSS_HYST on Elba, which is used to provide the net effect of mechanical force hysteresis in the Force Sensing Switch membrane keypad used in some morphing phones. This connection is different from P0.
GPO2 - The signal on Elba is being called TNLC_RESET. This is the reset line to the morphing peripheral. This connection is different from P0.
32kHz clock is required only for Solomon solution and not required for Pelikon solution.

## Slide 15
Elba Local Haptics
Haptics is needed for two specific uses cases, namely
a) Multimedia games force feedback
b) keypress tactile feedback
Elba uses a “FSR Membrane Switch” as the keypad. This material does not provide any tactile
feedback to the user when a key is pressed, unlike the “metal dome keypad”. Hence, a haptics
feedback is necessary for keypress.
Elba uses a new type of vibrator called the “piezoelectric transducer”.

## Slide 16
Linear Vib.
The linear vibrator is driven by a 2.5W Class-D audio Power Amplifier (PA) from
TI (P/No.: TPA2010) .This PA allows independent gain settings while summing signals from separate
sources. It can be configured to operate either in the differential or single ended mode.
In Elba, the PA is designed to operate in the single ended mode and the signal is driving
through the negative differential input (INNEG) from LSPL (pin U5) of the Atlas IC (U900). LSPL is the
left channel of the loudspeaker.
Linear
vibrator
U3_RTS_B
TPA2010D1
51R09731C42
INPOS
INNEG
PVDD
VDD
VOPOS
VONEG
GND1
GND2
33pF
0.1uF
SCM-A11
U5
C1
C2
C3
A3
B1
B2
A2
B3
LSPL
SHUTDOWN
0.1uF
0.1uF
ATLAS
LSPL
U5
C1
A1
C2
C3
A3
B1
B2
A2
B3
LSPL
100K 160K
62K
LIN_VIB_AMP_EN
C17
10K
R4
160K
R5
160K

## Slide 17
RF System Block Diagram
Bluetooth
TI 6035
Supply Lines
Control Lines
RF Signal Lines
LF Analogue
B+
PM (Atlas)
VRFREF
(2.775V)
VRF1
(2.775V)
VRF2
(2.775V)
VRFCP
(2.775V)
VRDIG
(1.875V)
TOUT7
Raptor
TransAAM
Quad
band
SAW
Filter
Antenna
Switch
US_EURO
LB_HB
TX_EN
TX_ANT_EN
IPC_BCM
HB_OUT
LB_OUT
CEL
EGSM
DCS
PCS
VRAMP
VDETECT
RESETB
SYSCLK
SYSCLKEN
STROBE
RXTXDATA
RXTXEN
CTRLCLK
CTRLDATA
CTRLEN
DBG_DATA
BTCLK
BTCLKEN
DIGRF_TXD
DIGRF_TXE
DIGRF_CCLK
DIGRF_CDAT
DIGRF_CEN
BB
Processor
SCM-A11
VBTRF
VIOLO
BT_RESET_B
26MHz
XTAL
EXTAL

## Slide 18
Audio Block

## Slide 19
U200
GSM PA – Low/ High Band
The Raptor module is a input/output, quad-band, dual-mode, GMSK/8PSK(EDGE) PA module
+ integrated Antenna swith circuit, intended for 2.75G radio applications. The module consists of a
dual line-up power amplifier, harmonic filter, logarithmic power detector, and analog power control circuit.
This PA module is used in the final amplification stages in a GSM portable telephone operating in either
GMSK or EDGE mode.
· EDGE Class 12 operation
· GMSK power class 4 operation in the GSM850 and EGSM900 bands
· GMSK power class 1 operation in the DCS1800 and PCS1900 bands
· EDGE power class E2 operaton

## Slide 20
U100
GSM Tranceiver Circuit „TransAAM“
Quad band GSM/EDGE transceiver solution consisting of Fractional-N synthesizer, VLIF (122,7kHz) RX front end,
GSM/EDGE TX modulator, power amplifier control circuitry, auto calibration functions, signal processing and auto
sequencing functions. The TX modulator functions are completely contained within the module.
The RX circuitry includes all circuitry required to convert RF inputs into digital I and Q signals. The baseband interface
consists of a serial control and serial data configuration that can function in both full DigRF and Neptune compatible
modes. The module requires the Raptor or Ophee PA and Saw filters to complete the RF solution.
Notes: <number>
<footer>
<header>
<date/time>
High-level chipset partitioning
Chipset walk-through

## Slide 21: Atlas
ATLAS Block overview

## Slide 22: U900
The Atlas is designed as Power Control Audio Power IC used in cellular transceivers.
Atlas will handle the audio and power management requirements for the system such like USB, Regulators, Charger Interface, Audio Codec; LED Sink circuit, RTC Interface.
The Circuit is in a 247 pin 0.5mm pitch 10x10 Ball Grid Array (BGA) Package.
Atlas 3.5 Power Control - Audio Power

## Slide 23: Charger
Charge Control Interface
Battery Connector
ESD Protection
Dual Charge Transistor
Curret Sense Resistor
Battery to B+ Switch
VBUS to B+ Switch
ESD Protection
Micro USB Connector

## Slide 24: SCMA11 / MXC91231
ARGON-LV
MXC91321
SCMA11
MXC91231
2.75G baseband processor
  Targeted for Single Core Modem Architecture
  key additional features include USB high-speed
ARM1136JFS
  400 MHz / 532 MHz in turbo mode
  16 kB L1 Instruction / 16 kB Data L1 Cache + 128 kB unified L2 cache
Starcore SC140
  204MHz / 250MHz in turbo mode.
  16 kB L1 Instruction / 32 kB L1 Data
SDMA
  133 MHz
CMOS90
15x15 468 MBGA
15x15 468 MBGA PoP
Notes: <number>
<footer>
<header>
<date/time>
High-level chipset partitioning
Chipset walk-through

## Slide 25: SCMA11 block

## Slide 26: ARM11 platform features
Industry standard ARM1136JF-S CPU
L1-cache: 16 KByte inst. and 16 KByte data
L2-cache: 128 KByte combined @ 133 MHz
M2 RAM: 16 KByte on-chip @ 133 MHz
M2 ROM: 32 KByte (Boot)
MAX: Multi Advanced High-Performance (AHB) Crossbar switch
Two clock domains bridged by L2CC
Notes: ARM11 platform walk-through
Two clock domains: core+L1 memory and AHB bus
ARM11 platform also used in other Freescale ICs (MXC275, i.MX31)
ETM and Nexus trace modules: different features, different tool suites
Crossbar switch (MAX) optimizes bus throughput

## Slide 27: SC140 platform
SC140e
  208MHz (250MHz in turbo mode)
  Interrupt Controller
Cache
  32 kB L1 D cache
  16 kB L2 I cache
  128 kB L2 unified cache
  32 kB M1 RAM
On-chip memory
  32 kB M1 RAM
  1 MB M2 ROM
  640 kB M2 RAM

## Slide 28: U500
Serializer
Low voltage/ Low current High Speed Serial interface
• 26 bit dual strobe ultra low power serializer/deserializer
• Dual Power Supplies: Core Supply: 2.5 to 3.0V Parallel I/O Supply 1.6 to 3.0V
• Single device to operate as serializer or deserializer
• Standby Power-Down mode support
• Package: 42uBGA 3.5mm x 4.5mm with 0.5mm Ball Grid Pitch

## Slide 29: U300
Bluetooth Class 2.0
The BRF6300 chip is a highly integrated single-chip CMOS (CO27 process) Bluetooth device that forms
a complete standalone Bluetooth wireless communication system. The BRF6300 is based on the
BRF6150 and is pin-to-pin backwards compatible with the BRF6150 device when VDD_IO of 1.8V is
used and not using crystal. The BRF6300 is the third generation of Texas Instruments' single chip BT
device, succeeding the BRF6150 and the BRF6100 devices.
This device implements an advanced solution for the Bluetooth protocol with easy interfacing to a host
system.

## Slide 30
Test requirements
Service Test Issue: RFMD Prime Impact
 | In 2007 and 2008 Motorola plans to ship 21.5 million EDGE capable phones with the RFMD RF chip globally. When these phones are returned to Motorola service only two test sets will be capable of EDGE phasing. After a level 3/4 board repair, all phones must be re-phased to ensure the phone meets factory specifications. Only supporting two test sets may cause some regions to reroute level 3 or level 4 repairs for phones using RFMD Prime to service centers which have capable test equipment.
Bulletin: LVCCFSB2007 - 203

## Slide 31: Data Block Signing
1. When will the service solution be available
Right now the project is in the coding phase, which is scheduled from June 1 to July 12. After testing is finished, deployment should begin around August 23. The main bottleneck in the process is the web service. The client tool will most likely be finished well before that date, but the client will not be able to be used in the service centers until the web service is up and accessible.
2. What phone types are infected by in moment
At the moment the only released phone that supports DBS is the Z6 and V8, and I'm not sure when the next one is scheduled to SA. The last I had heard, all LinuxJava platform phones will support DBS.
3. What data will be handled by the process (IMEI, Lock Codes, ...?)
I think the Z6 supports IMEI only, but Subsidy Lock DBS blocks should also be supported soon for new models. I have seen documentation that mentioned that Factory State, Bootloader, and Secure Test Command may be the next types of DBS data after those two, but I'm not sure of what the status is for those new data types.
4. What kind of applications will support that? (RadioCom, Repair Studio....?)
As far as I know, the only tool currently developed to use the DBS web service is my own standalone tool. The RSD team is currently working on adding web service support for the Device Unlock web service, but I don't think they are planning to add support for the DBS web service yet. Also, any STE framework UIs will have access to the DBS functionality through the framework, so MotoGate or MotoAnalyzer could easily add DBS once my standalone tool is deployed.
5. Does any Service Centre need a Hardware Token to run a PKI Server?
To do Data Block Signing, a service center needs three things: a hardware token, a software certificate, and an LDAP account that is registered on the DBS web service. These are the same as the requirements of the existing secure web services, such as the DRM web service and the Device Unlock web service